## Slide 1: CE-QUAL-W2 Workshop, 2024 Introduction to Modeling
Todd Steissberg, PhD, PE
U.S. Army Engineer Research and Development Center, Environmental Laboratory
CE-QUAL-W2 Workshop
July 08 – 09, 2024
UNCLASSIFIED
UNCLASSIFIED
Environmental Systems
Modeling Team

## Slide 2: Systems Modeling: Guiding Principles
George Box:
  ... all models are approximations. Essentially, all models are wrong, but some are useful. However, the approximate nature of the model must always be borne in mind....
  Paraphrased:
    “All models are wrong, but some are useful.”
Albert Einstein:
  It can scarcely be denied that the supreme goal of all theory is to make the irreducible basic elements as simple and as few as possible without having to surrender the adequate representation of a single datum of experience.
  Paraphrased:
    “Everything should be made as simple as possible, but no simpler.”
Hans Albert Einstein (Hydraulic Engineer):
  You can assume anything you want. The water won’t!
  Moral: Be careful with your assumptions.
Albert Einstein, said of his son’s career, “He is working on a more difficult problem.”

## Slide 3: The Tea Leaf Paradox
Question: When you stir a cup of tea with tea leaves in the bottom of the cup, do they move towards the center of the cup or towards the sides?

## Slide 4: The Tea Leaf Paradox
Question: When you stir a cup of tea with tea leaves in the bottom of the cup, do they move towards the center of the cup or towards the sides?
It seems simple: centrifugal force should cause the tea leaves to collect along the sides of the cup. But do they?

## Slide 5: The Tea Leaf Paradox
Question: When you stir a cup of tea with tea leaves in the bottom of the cup, do they move towards the center of the cup or towards the sides?
It seems simple: centrifugal force should cause the tea leaves to collect along the sides of the cup. But do they?
Albert Einstein solved this problem in 1926 in a paper he wrote on meandering rivers. Einstein was the first person to describe how helical flow helps to determine the length and migration of meander bends in rivers.

## Slide 6: The Tea Leaf Paradox
Question: When you stir a cup of tea with tea leaves in the bottom of the cup, do they move towards the center of the cup or towards the sides?
It seems simple: centrifugal force should cause the tea leaves to collect along the sides of the cup. But do they?
Albert Einstein solved this problem in 1926 in a paper he wrote on meandering rivers. Einstein was the first person to describe how helical flow helps to determine the length and migration of meander bends in rivers.
Amazon River, 1985
Amazon River, 2014
https:earthobservatory.nasa.gov

## Slide 7: Modeling Definitions
Mathematical modeling is the process of developing a mathematical representation of a system using mathematical concepts and techniques to describe the processes, interactions, and parameters of that system.
Computer modeling is the process of developing mathematical algorithms that describe a system and then developing the computer code to simulate them.
Modeling vs. Simulation:
  Modeling is the process of building a model
  Simulation is the process of using a mathematical model to study the behavior of a system for a particular time period.
Source: https://en.wikipedia.org/wiki/Flowchart

## Slide 8: Modeling Definitions
Empirical modeling uses an inductive approach, based on observations (data) and the relationships between system components, such as determined through linear and non-linear regression.
Mechanistic (process-based) models use a deductive approach, based on the principles of physics, chemistry, and biology.
Most water quality models use a mixture of empirically-derived relationships combined with iterative calculations that describe the physical and biogeochemical processes.
Source: Steven C. Chapra (1997). Surface Water-Quality Modeling. Waveland Press, Long Grove, IL.

## Slide 9: Computer Models & Programming
Early computer models were custom-developed applications programmed for a specific purpose, such as a water quality model of a particular lake or reservoir.
The first mathematical water quality model was developed by Streeter and Phelps in 1925. It predicted the dissolved oxygen “sag curve” in rivers.
In the 1960’s, computer models began to be developed. By the early 1970’s, general-purpose models began to emerge.
Today’s general-purpose water resources models, e.g., HEC-RAS, HEC-ResSim, and CE-QUAL-W2, typically do not require the modeler to do any programming.
  CE-QUAL-W2 is a general-purpose model, but it allows custom computations through modifying and enhancing the source code.
  HEC-ResSim allows custom computations through “scripting.” Modelers cannot alter the source code.
  Scripting (Python, R, MATLAB) is increasingly used for visualization and analysis of the results.
A 48-hour computer simulation of Typhoon Mawar using the Weather Research and Forecasting model.
Source:
https://en.wikipedia.org/wiki/Computer_simulation

## Slide 10: Water Quality Modeling
Water quality modeling combines mathematical descriptions of the physical and biogeochemical processes to characterize behavior of a waterbody or water resource.
Water resource and water quality models have been developed to understand and predict the processes in reservoirs, rivers, and watershed runoff.
The following fields comprise the body of knowledge required for accurate water quality modeling and analysis:
  Hydrodynamics (physical limnology)
  Meteorology
  Aquatic chemistry (chemical limnology)
  Aquatic biology (biological limnology)
  Geology (sedimentation, sediment settling, resuspension, and transport)
  Mathematics and numerical methods
  Statistics
Flows influence water quality
Water quality must influence flows

## Slide 11: Benefits of Water Quality Modeling
Interpolation
  Observed data is sparse in space and time.
  Interpolation addresses questions like:
    Where are the best locations for sampling?
    Where are the most severe water quality problems occurring?
Extrapolation
  Forecast water quality in the future.
  Predict water quality for different water management scenarios
  Extrapolation answers questions like:
    How will the watershed function under different climate forcing conditions?
    How will the ecosystem respond if flow allocations are changed, hydropower withdrawals increased, and releases altered to meet ecosystem restoration targets (e-flows)?
Improved understanding of the system.
Dworshak Dam, Idaho
Detroit Dam, Oregon

## Slide 12: Reservoir Processes and Zones
Riverine zone
  River-like flows within channel
  Minimum requirement: 1D river model (segments)
Lacustrine zone
  Lake-like system, vertically stratified, slow flows
  Minimum requirement: 1D reservoir model (layers)
Transition zone
  Stratification and downstream flows important
  Minimum requirement: 2D model (layers and segments)
Reservoir system with important flow, WQ, and ecosystem processes for each of three zones.
Notes:
1D river model used for channels in a reservoir system
2D river model used for floodplain simulation
2D reservoir model used for large stratified reservoirs
Riverine
Transition
Lacustrine
Graphic by Lauren Melendez

## Slide 13: Model Dimensions, River-Reservoir System
Unstratified river/reservoir reaches:
  May be modeled as 1D water bodies (segments)
Stratified reaches:
  May be modeled as 1D reservoirs (layers) for real-time release decision-making to meet downstream objectives
  To characterize and understand in-reservoir processes, reservoirs need to be modeled as 2D water bodies (layers and segments)
    Ensures accuracy, capturing important in-reservoir processes (mixing, pollutants, inflows, etc.)
    Identifies vulnerabilities and restoration/management options (e.g., velocities and temperature for HAB management)
1D River
2D Reservoir
1D Reservoir
1D River
2D Reservoir
1D Reservoir
Graphics by Lauren Melendez

## Slide 14: Model Dimensions: River-Floodplain System
Unstratified river channels are often modeled as 1D water bodies, varying from upstream to downstream
Hydrologic connectivity across the floodplain is important
Floodplains need to be modeled as 2D water bodies, varying in all directions across the landscape
1D River (Channel)
2D River (Floodplain, Wetlands)
Graphics by Lauren Melendez

## Slide 15: Introduction to CE-QUAL-W2
CE‐QUAL‐W2 is a two‐dimensional (2D), longitudinal/vertical, hydrodynamics and water quality model.
It enables characterization of the vertical and longitudinal changes in a reservoir.
The model assumes the reservoir is ”well mixed” laterally, with no variation from one side of the channel to the other in a given layer (vertical) and segment (longitudinal).
Since CE-QUAL-W2 assumes lateral homogeneity, it is especially suited for relatively long and narrow waterbodies that exhibit longitudinal and vertical water quality gradients.
CE-QUAL-W2 has been applied to rivers, lakes, reservoirs, estuaries, and combinations thereof.
Longitudinal view of temperature output for a riverine section, reservoir, and estuary, from a CE‐QUAL‐W2 model application.

## Slide 16: CE-QUAL-W2 Applications
CE-QUAL-W2 is the reservoir water quality (WQ) model of choice throughout the U.S. and many other countries
CE-QUAL-W2 is the two-dimensional (2D), longitudinal/vertical hydrodynamic and water quality model of choice for the following agencies:
  U.S. Army Corps of Engineers (USACE)
  U.S. Geological Survey (USGS)
  U.S. Bureau of Reclamation (USBR)
  U.S. Environmental Protection Agency (EPA)
  Tennessee Valley Authority (TVA)
There have been more than 300 applications worldwide of CE-QUAL-W2
Cited in more than:
  15 PhD dissertations
  50 Master’s theses
  100 presentations at scientific meetings
  20 journal articles worldwide

## Slide 17: CE-QUAL-W2 Capabilities
Longitudinal-vertical hydrodynamics and water quality in stratified and non-stratified systems
Interactions between nutrients, dissolved oxygen, and organic matter
Fish habitat volume
Selective withdrawal from specially design outlets to provide cold-water releases from stratified reservoirs
Hypolimnetic aeration
Multiple algae, epiphyton/periphyton, zooplankton, and macrophyte groups
CBOD
Sediment diagenesis model
Generic water quality groups
Internal dynamic pipe/culvert model
Hydraulic structures (weirs, spillways) algorithms

## Slide 18: CE-QUAL-W2 Capabilities, Continued
The hydraulic structures algorithms include submerged and two-way flow over submerged hydraulic structures as well as a dynamic shading algorithm based on topographic and vegetative cover.
Variable density as affected by temperature, salinity, Total Dissolved Solids (TDS), and Total Suspended Solids (TSS) to simulate stratified flow.
28 water quality constituent state variables
  Any combination of constituents can be included or excluded from a simulation.
  The effects of salinity or total dissolved solids/salinity on density, and thus hydrodynamics, are included only when simulated in the water quality module.
  The water quality algorithm is modular, allowing constituents to be easily added as additional subroutines.

## Slide 19: Acknowledgements
Development:
Scott Wells, Portland State University
Chris Berger, Portland State University
Zhonglong, Zhang, Portland State University
Isaac Mudge, USACE New Orleans District
Funding and Support:
USACE Numerical Model Maintenance Program, Hydraulics, Hydrology, and Coastal Community of Practice (HH&C CoP)
Ecosystem Management and Restoration Research Program (EMRRP)
Aquatic Nuisance Species Research Program (ANSRP)
Graphics by Lauren Melendez

## Slide 20: Questions?