## Slide 1: WATER QUALITY MODELING
DISCOVER | DEVELOP | DELIVER
Todd Steissberg
U.S. Army Engineer Research and Development Center, Environmental Laboratory
CE-QUAL-W2 Workshop
July 08-09, 2024
1
UNCLASSIFIED
UNCLASSIFIED

## Slide 2: Outline
Concept/Background
Schematic
Assumptions
  Mass Balance
  Conservative
  Complete Process Representation
Water quality capabilities
  State variables
  Derived variables
  WQ processes

## Slide 3: Water Quality
Water quality is agglomeration of physical, chemical, and biological components of water column that determine its overall “condition.”
Physical components include temperature and suspended solids and conservative dissolved
substances.
Chemical components include dissolved substances whose levels are impacted by physical,
chemical , and biological processes.
Biological components are living organisms whose normal biological processes are impacted by and have impacts on the conditions present in the water column.

## Slide 4
Conceptual Water Quality Model
Qin
Qout
Cin
C
C
V
change in mass over time
total inflow of mass
total outflow of mass
𝑑𝑡
𝑑𝑉
= σ 𝑄𝑖𝑛 - σ 𝑄𝑜𝑢𝑡
𝑑𝐶𝑉
𝑑𝑡
= σ 𝑄𝑖𝑛 𝐶𝑖𝑛 - σ 𝑄𝑜𝑢𝑡 𝐶
+ 𝑟 𝑉
kinetic transformations

## Slide 5: CE-QUAL-W2 Water Quality


+ +
 t  x  z
-
 BD 
 x
-
 BD 
 z
x  x 
z  z 
 B  UB  WB
= q B +
S B
c
y=y1
y=y2
c
Laterally averaging
Kinetics

## Slide 6: Mass Balance
Mass of all substances in model is conserved, not created nor destroyed.
Mass can be transformed from one form to another (i.e., Nitrogen from NH4 to NO2/NO3 to N2)
Mass can enter and leave model by specified processes and means.
Important that our representation of process is thorough and complete as possible

## Slide 7: Conservation
The mass of all substances in model is conserved, not created nor destroyed.
Assumption is crucial to our use of model and interpretation of its results.
Important that our representation of process is thorough and complete as possible.
Specified process rates should be supported by data or from technical literature.

## Slide 8: CE-QUAL-W2 Water Quality
Arbitrary Constituents
Inorganic suspended solids groups
CH4, H2S
N2, DGP, TDG
Labile and refractory dissolved organic matter groups (DOM, DOC, DON, DOP)
Labile and refractory particulate organic matter fractions (POM, POC, PON, POP)
Dissolved and particulate silica
Alkalinity, Total inorganic carbon (TIC), PH
Different algal groups
NH4-N, NO3-N+NO2-N
PO4-P
Fe, Mn
CBOD groups
Sediment diagenesis model
SYSTDG

## Slide 9: CE-QUAL-W2 DOM

## Slide 10: CE-QUAL-W2 POM

## Slide 11: CE-QUAL-W2 Ammonium

## Slide 12: CE-QUAL-W2 Nitrate/Nitrite

## Slide 13: CE-QUAL-W2 Phosphate

## Slide 14: CE-QUAL-W2 DO

## Slide 15: CE-QUAL-W2 Algae

## Slide 16: CE-QUAL-W2 Bed Sediment – First Order Approach

## Slide 17: CE-QUAL-W2 Bed Sediment – Sediment Diagenesis Model

## Slide 18: Conversions between CE-QUAL-W2 State Variables and Commonly Used Field Data

## Slide 19: Questions?
US Army Corps of Engineers 
UNCLASSIFIED
Engineer Research and Development Center
UNCLASSIFIED
19