## Slide 1: WATER QUALITY MODELING
DISCOVER | DEVELOP | DELIVER
Todd Steissberg
U.S. Army Engineer Research and Development Center, Environmental Laboratory
CE-QUAL-W2 Workshop, 2024
July 08-09, 2024
1
UNCLASSIFIED
UNCLASSIFIED
Environmental Systems
Modeling Team

## Slide 2: Outline
Important Terms
Water Quality Definition
Conceptual Model
Assumptions
  Mass Balance
  Conservative
  Complete Process Representation
Water quality capabilities
  State variables
  Derived variables
  WQ processes

## Slide 3: Important Terms
State Variables: Fundamental variables in a model that describe the state of the system at any given time. These variables are intrinsic to the system and are typically governed by differential equations representing the physical, chemical, or biological processes. In other words, they are incorporated into the advection-diffusion and transformation processes.
  Examples: Concentrations of various substances (e.g., nutrients like nitrogen and phosphorus, dissolved oxygen, temperature, microbial populations).
Derived Variables: Calculated from the state variables and other known quantities within the system. They provide additional insights or outputs that are not directly modeled by the state equations but are important for interpreting the system's behavior.
  Examples: Saturation levels of dissolved oxygen (derived from temperature and oxygen concentration), water quality indices (calculated from various state variables), and total suspended solids (which might be derived from measurements of turbidity and flow rates), and Total Dissolved Gas (TDG, derived by summing dissolved oxygen and nitrogen)

## Slide 4: Important Terms, Continued
Conservative Constituents: Do not undergo any chemical, biological, or physical transformation as they move through the system. Their concentration changes only due to dilution, mixing, or advection.
  Examples: Chloride, sodium, and other non-reactive tracers or substances. These substances can be used to track water movement and mixing patterns without altering their properties.
Non-Conservative Constituents: Undergo chemical, biological, or physical transformations as they move through the system. Their concentration changes due to processes such as chemical reactions, biological uptake or release, and physical transformations.
  Examples: Nutrients like nitrate and phosphate (subject to biological uptake and transformation), organic matter (subject to decomposition), and pollutants like heavy metals (which can adsorb to sediments or precipitate).

## Slide 5: Water Quality
Water quality is agglomeration of physical, chemical, and biological components of water column that determine its overall “condition.”
Physical components include temperature and suspended solids and conservative dissolved
substances.
Chemical components include dissolved substances whose levels are impacted by physical,
chemical , and biological processes (non-conservative).
Biological components are living organisms whose normal biological processes are impacted by and have impacts on the conditions present in the water column.

## Slide 6
Conceptual Water Quality Model
Qin
Qout
Cin
C
C
V
change in mass over time
total inflow of mass
total outflow of mass
𝑑𝑡
𝑑𝑉
= σ 𝑄𝑖𝑛 - σ 𝑄𝑜𝑢𝑡
𝑑𝐶𝑉
𝑑𝑡
= σ 𝑄𝑖𝑛 𝐶𝑖𝑛 - σ 𝑄𝑜𝑢𝑡 𝐶
+ 𝑟 𝑉
kinetic transformations

## Slide 7: CE-QUAL-W2 Water Quality


+ +
 t  x  z
-
 BD 
 x
-
 BD 
 z
x  x 
z  z 
 B  UB  WB
= q B +
S B
c
y=y1
y=y2
c
Laterally averaging
Kinetics

## Slide 8: Mass Balance
Mass of all substances in model is conserved, not created nor destroyed.
Mass can be transformed from one form to another (i.e., Nitrogen from NH4 to NO2/NO3 to N2)
Mass can enter and leave model by specified processes and means.
Important that our representation of process is thorough and complete as possible

## Slide 9: Conservation
The mass of all substances in model is conserved, not created nor destroyed.
Assumption is crucial to our use of model and interpretation of its results.
Important that our representation of process is thorough and complete as possible.
Specified process rates should be supported by data or from technical literature.

## Slide 10: CE-QUAL-W2 Water Quality
Arbitrary Constituents
Inorganic suspended solids groups
CH4, H2S
N2, DGP, TDG
Labile and refractory dissolved organic matter groups (DOM, DOC, DON, DOP)
Labile and refractory particulate organic matter fractions (POM, POC, PON, POP)
Dissolved and particulate silica
Alkalinity, Total inorganic carbon (TIC), PH
Different algal groups
NH4-N, NO3-N+NO2-N
PO4-P
Fe, Mn
CBOD groups
Sediment diagenesis model
SYSTDG

## Slide 11: CE-QUAL-W2 Dissolved Organic Matter (DOM)

## Slide 12: CE-QUAL-W2 Particulate Organic Matter (POM)

## Slide 13: CE-QUAL-W2 Ammonium

## Slide 14: CE-QUAL-W2 Nitrate/Nitrite

## Slide 15: CE-QUAL-W2 Phosphate

## Slide 16: CE-QUAL-W2 Dissolved Oxygen (DO)

## Slide 17: CE-QUAL-W2 Algae

## Slide 18: CE-QUAL-W2 Bed Sediment – First Order Approach
Notes: In water quality modeling, first-order and second-order approaches refer to the types of differential equations and reaction kinetics used to describe the rates of processes affecting water quality constituents. These approaches are commonly applied to model the transformation and degradation of pollutants or substances in water bodies.
First-Order Approach
Definition:
- In a first-order approach, the rate of change of a substance concentration is directly proportional to the concentration of the substance itself. This approach is characterized by a linear relationship.
Mathematical Representation:
The general form of a first-order reaction rate equation is:
dC/dt= -kC
where:
- C is the concentration of the substance
- t is time
- k is the first-order rate constant (with units of time-1)
Characteristics:
- Linear Kinetics: The rate of decay or transformation of the substance decreases linearly with decreasing concentration.
- Simplified Assumptions: Assumes that other factors affecting the reaction rate are constant and do not change with time or concentration.
- Common Applications: Often used for modeling the decay of pollutants like organic contaminants, radioactive decay, and certain microbial processes.
Example:
The degradation of a pollutant in a river where the rate of decay depends solely on the pollutant concentration and a constant rate coefficient.
Second-Order Approach
Definition:
In a second-order approach, the rate of change of a substance concentration is proportional to the square of the concentration of the substance or the product of the concentrations of two reacting substances. This approach involves a quadratic relationship.
Mathematical Representation:
The general form of a second-order reaction rate equation can be:
dC/dt = -kC^2
for a single substance, or
d[A]/dt = -k[A][B]
where:
- [A] and [B] are the concentrations of the reacting substances
- t is time
- k is the second-order rate constant (with units of concentration-1 and time-1)
Characteristics:
- Quadratic Kinetics: The rate of reaction changes more rapidly as concentrations change, leading to non-linear dynamics.
- Interaction of Substances: Often involves interactions between two different substances or molecules.
- Complex Behavior: Can better represent more complex reactions where the rate is influenced by the concentrations of multiple reactants.
- Common Applications: Used for modeling processes like the reaction between dissolved oxygen and organic matter (biochemical oxygen demand), and the interaction between different pollutants or nutrients in water.
Example:
- The reaction between dissolved oxygen and organic matter in a water body where the rate of oxygen consumption depends on both the oxygen concentration and the organic matter concentration.
Key Differences
1. Order of Reaction:
- First-Order: Rate depends linearly on the concentration of one substance.
- Second-Order: Rate depends quadratically on the concentration of one substance or linearly on the product of the concentrations of two substances.
2. Rate Constants:
- First-Order: Has units of time-1
- Second-Order: Has units of concentration-1 and time-1
3. Application Context:
- First-Order: Simplified, often for single-substance decay or simple microbial processes.
- Second-Order: More complex, often for reactions involving two substances or more intricate processes.
4. Modeling Complexity:
- First-Order: Easier to implement and solve due to its linear nature.
- Second-Order: More complex to implement and solve due to its non-linear nature.

## Slide 19: CE-QUAL-W2 Bed Sediment – Sediment Diagenesis Model

## Slide 20: Conversions between CE-QUAL-W2 State Variables and Commonly Used Field Data

## Slide 21: Data Limitations
Availability and Quality of Data:
  Insufficient Data: Lack of historical or real-time data for model calibration and validation.
  Data Quality: Inaccuracies and inconsistencies in data collection methods, leading to unreliable inputs.
  Spatial and Temporal Resolution: Inadequate resolution of data to capture local variations and short-term dynamics.
Missing Data: Gaps in data records can impede the development of accurate models.

## Slide 22: Model Complexity and Assumptions
Simplified Representations:
  Models often simplify complex physical, chemical, and biological processes, which can lead to oversimplification and loss of important details.
  Assumptions and approximations may not always reflect real-world conditions accurately.
Parameter Estimation:
  Difficulty in accurately estimating model parameters due to variability and uncertainty in natural systems.
  Sensitivity of models to parameter values can lead to significant variations in output.

## Slide 23: Questions?
US Army Corps of Engineers 
UNCLASSIFIED
Engineer Research and Development Center
UNCLASSIFIED
19